## Slide 1: Arduino Based Solar Cell TestPlatform
HFDA
2013

## Slide 2: Idea
Making a small, affordable platform, that can take systematic data from a solar cell under test
Enable taking IV curves (range from +-2V)
Log IV curve, Irradiance, Temperature (both cell and air), Time
Store on SD card and/or ethernet (www.cosm.com?) or pc.
Use directly with pc as a Keithley 2400 or as a headless standalone unit

## Slide 3: Design Specs
Based on the IV tester of the MIT guys
Make Arduino sketch for my setup of IV scan:
1. Use MCP4728 DAC for setting the voltage output
  feed output to channel A and B on OPAMP (enabling negative and positive part of sweep)
  Channel C could be used for negatively biasing a photodiode (Intensity)
2. Use MCP3424 ADC for measuring current and voltage
  12/14/16bit with four channels differentially
  enables measurement of voltage over DUT, R_shunt and OP_AMP
  Last channel could be used for photodiode (Voltage over R_shunt or bolometer which is in mV)
3. DHT11 or DHT22 incorporation for environment conditions
x. Temperature sensor DS18 one wire
x. SD-card storage of files instead of serial (stand alone tester)
x. Ethernet connection
x. RTC chip with temp readout
used for storing data no sd-card with filenames for date and time
X. sleep mode with RTC wakeup

## Slide 4: Diagram
Top layer
Bottom layer

## Slide 5: Software (embedded)
########### Implementing software ##############
include libraries:
Wire
MCP4728
MCP3424
SD
OneWire
DallasTemperature
DHT
Ethernet
Defining variables
Setting std range of -1V to 1V
Setting common voltage on Va and Vb to 1.5V
Setting # points = 200

## Slide 6: Components